## Slide 1: Run2 TDC main function test
Jin-Yuan Wu, Grass Wang
Da-Shung Su, Wen-Cheng Chang
2012/Oct/02

## Slide 2: New Design
We started it from scratch, only keep the FPGA input/output port.
The new TDC is based on multi-sampling principle. The TDC card records hits only, so that we don’t need zero suppression.

## Slide 3: Circular Buffer Timing Window
The hits in the Register-Pipe are written to the circular buffer every 64 ns per hit.
If the Register-Pipe is filled with 4 hits, it takes 256 ns to write them into circular buffer.
The hits stored in Register-Pipe (RegPipe4a) blocks are readout when Load (LD)=1, every 4 clock cycles at 62.5 MHz and the hits being readout are cleared at the end of Load (LD)=1 pulse when AllShift=1 for 1 cycle at 250 MHz.
Data from a group of 4 channels are written into one of the 2 (or 4, 8) circular buffers i(SRAM256x16 ) to wait for trigger.
LD
D
WA
LD
D
RA
LD
TCQ
AllShift
CK250
CK62
TFQ
RegPipe4a
SRAM256x16

## Slide 4: Number of Circular Buffers
0
1
2
3
4
5
6
7
WA/RA
WA[4:0]
WBK[0:2]
SEL[7:5]=000
WA[5:0]
WBK[0:1]
SEL[7:5]=001
WA[6:0]
WBK[0]
SEL[7:5]=011
Data from a group of 4 channels are written into one of the 2 (or 4, 8) circular buffers (SRAM256x16) to wait for trigger.
Number of circular buffer is controlled by the users using register bits SEL[7:5], only three bit pattern are supported at this time.
These buffer size corresponding to hit accepting window of 512, 1024 and 2048 ns. Due to effect of the Register-Pipe, the 100% hit accepting windows are 256 ns narrower.
When a trigger arrives, writing address are pointed to the next circular buffer and the current circular buffer is readout.
The readout address follows the same circular buffer setting.
The times needed to copy hits from circular buffer to event buffer, i.e., the copy in progress (CIP) times are shown above.
SEL [7:5] | Number of Circular Buffers | Circular Buffer Size | Buffer Timing Window | CIP Time
000 | 8 | 32 | 512 ns (-256 ns) | 32 x 16 x 16 ns = 8 us
001 | 4 | 64 | 1024 ns (-256 ns) | 64 x 16 x 16 ns = 16 us
011 | 2 | 128 | 2048 ns (-256 ns) | 128 x 16 x 16 ns = 32 us

## Slide 5: Event Buffer Configuration
0
1
2
3
4
5
6
7
8
9
WA
CNT[4:0]
Nevt[0:4]
CNT[5:0]
Nevt[0:3]
CNT[6:0]
Nevt[0:2]
CNT[7:0]
Nevt[0:1]
CNT[8:0]
Nevt[0]
CNT[9:0]
M[2:0]=0
M[2:0]=1
M[2:0]=2
M[2:0]=3
M[2:0]=4
M[2:0]=5
The total size of the event buffer is 1024 x 32-bit words. It can be configured by the users into 1, 2, 4, 8, 16, 32 blocks each storing an event.
The event buffer can be read and written from VME interface.
The module can be retriggered while VME is reading out previous events. The new events will be copied into different event blocks.
If too many triggers are sent to module within short time interval, old events will be overwritten. The trigger system should be designed to prevent overwritten from happening.
M[2:0] | Number of events | Max. number of words/event
5 | 32 | 32
4 | 16 | 64
3 | 8 | 128
2 | 4 | 256
1 | 2 | 512
0 | 1 | 1024

## Slide 6: Event Buffer Layout
0
1
2
3
4
5
6
7
8
9
WA
CNT[4:0]
Nevt[0:4]
CNT[5:0]
Nevt[0:3]
CNT[6:0]
Nevt[0:2]
CNT[7:0]
Nevt[0:1]
CNT[8:0]
Nevt[0]
CNT[9:0]
M[2:0]=0
M[2:0]=1
M[2:0]=2
M[2:0]=3
M[2:0]=4
M[2:0]=5
The event buffer is subdivided as shown in the table.
The readout program in VME should address the event block in the sequence shown.

## Slide 7: data resolution
250 MHz clock
9 phases
~0.444 ns resolution
1 | 10.26% | 410.32
2 | 11.89% | 475.47
3 | 10.22% | 408.74
4 | 12.30% | 491.83
5 | 10.41% | 416.55
6 | 11.16% | 446.48
7 | 9.55% | 382.18
8 | 10.42% | 416.88
9 | 13.79% | 551.53

## Slide 8: Trigger time resolution
The trigger time resolution is same with the data resolution.
Trigger time - Data time = TDC time

## Slide 9: Current Design
Time resolution | ~0.44 ns
Two-hits resolution | 4 ns
Width of accepted window | 2us (user selected)
Edge detective | User selected leading edge only or both edges.
Maximum hits per trigger | User selected (32~1024)
Maximum events per IRQ | User selected (2~32)

## Slide 10: Register Map
0x000 version (e9061206)
0x004 CSR
0x008 test area
0x1000~0x1ffc = event buffer (1k internal)
0x2000~0x2ffc = test area
?~? = dual port buffer (32 k)
D31-D16 | D08 | D7-5 | D2-0
EN4X (CSR) | BothEdge (Edge selection) | SEL(READ/WRITE addr) | M (buffer size)

## Slide 11: DATA format
D15 | D14 | D13 | D12 | D11 | D10 | D09 | D08 | D07 | D06 | D05 | D04 | D03 | D02 | D01 | D0
Trig [15:3] (trigger time) |  |  |  |  |  |  |  |  |  |  |  | Fine time |  |  | 
D31 | D30 | D29 | D28 | D27 | D26 | D25 | D24 | D23 | D22 | D21 | D20 | D19 | D18 | D17 | D16
1 | CNT[10:0] (number of hits) |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | positive or negative edge
D31 | D30 | D29 | D28 | D27 | D26 | D25 | D24 | D23 | D22 | D21 | D20 | D19 | D18 | D17 | D16
Cable: 4,5,6,7 |  |  |  | Channel number: 0-15 |  |  |  | Hit Id |  |  |  | 0 | 0 | 0 | positive or negative edge
Header
Data
D15 | D14 | D13 | D12 | D11 | D10 | D09 | D08 | D07 | D06 | D05 | D04 | D03 | D02 | D01 | D0
TDC [15:4] (data time) |  |  |  |  |  |  |  |  |  |  |  | Fine time |  |  | 
Notes: MSB = most significant bit

## Slide 12: Main part test
fix tdc time, and apply cable-delay between each channel, with Multiple TDC in the VME-crate
  Check if there is cross-talk between different channels
  Check if tdc time stable in each channel
  Check free running-internal-clock
  Check if we drop any signal during the test
Shift signal to both edge of time window
  to see if tdc are stable around the edge
Multiple signals in each channel

## Slide 13: TDC main part test – Oct/2012

## Slide 14: Random hit test for internal free running clock

## Slide 15: TDC main part test – Oct/2012

## Slide 16: Cable delay between channels channel 0~7 = Channel 8~15
ch9
ch1
Ch1+Ch9

## Slide 17: Cable delay between channels
Ch8 -Ch0
Ch9 -Ch1
Ch10-Ch2
Ch11-Ch3
Ch12-Ch4
Ch13-Ch5
Ch14-Ch6
Ch15-Ch7
……
……
Ch31- ch16
Ch47-ch32
Ch63-ch48

## Slide 18: More test To do
Cosmic trigger (for real random hit test)
Calibration
Minimize the tdc time to check linearity problem (RMS of tdc vs ΔT)

## Slide 19: Where are we …
The time information of data and trigger are tested
Time line
  Sep/Oct: main-function test, building the production test system
  Nov 2012: add future designs – time window cut and delay
  Dec 2012 :Production test
    Time diff between diff channels
    Multiple pulses in each channel
    full system - test vme noice feedback, with 12 TDCs in one VME crate
  Jan 2013 :Fine tune with E906 detectors/cosmic ray

## Slide 20
Thank you…

## Slide 21
Backup

## Slide 22
Ch8-Ch0 Ch9-Ch1

## Slide 23: Random hit test for internal free running clock
Zoom in

## Slide 24: Random hit test for internal free running clock
Zoom in

## Slide 25: Data Throughput (worst case scenario)
Assume 100% occupancy each channel will output 4 Byte per event. (32 bits for and channel information of one hit)
For each card: 4*64 = 256 byte per event
For a system with 100 cards: 25.6KB per event
Assume trigger rate 2KHz : 51.2 MB/s (for only one card is 0.05 MB/s)
A Gigabit Ethernet support at 1 Gbps (1000 Mbps =125 MBps)
VME backplane speed for BLT32 =25MBytes/s (25Bytes/us) = (10 us to readout each TDC/event) (worst case scenario)
Notes: The old TDC without zero suppression is ~ 1k bytes per event, which took ~90us to read out

## Slide 26: Beam structure
Bin size =137 us
Dead time was 680 us in the Run1
If the deadtime is 90us (70 us?), the dead part will decrease a lot …
Before Inhibit
After Inhibit
137us bin size

## Slide 27: Real case
In the final run (2173) in Run1
The Max number of hit is less than 4000
In the worth case scenario, 4000 hits per events. For one event we get 4* 4000 =16KB
we were assumeing 25.6KB on last page
so that, in the real run, the deadtime is much lower than what we estimated

## Slide 28
CIP (copy in progress) free: 2~32 buffer to store data during CIP. Data still can be record during CIP.

## Slide 29
Transfer type | Speed
BLT32 | 25 MBytes/s
MBLT64 | 50 MBytes/s
2e VME | 88 MBytes/s

## Slide 30: User selected buffer size
Maximum hits per trigger (32~1024)
Maximum events per IRQ (1~32)

## Slide 31
Third layer buffer
Second layer buffer
First layer buffer

## Slide 32: 3 layers buffers
First layer buffer
second layer buffer
Third layer buffer

## Slide 33: First layer buffer
4 hits per channel,
  Buffer pushing: Any clock cycle at 250 MHz.
  Buffer popping: 1 hit/64 ns.
  RegPipe4a/ChGRP4a
Notes: nothing to do with trigger

## Slide 34: Second layer buffer
Second layer buffer, every 4 channels share a circular buffer
  (Page size)*(Number of Pages) = 256, user defined.
  Hits fill into a page continuously.
  When a trigger is received, hits are filled to next page and the current page is copied to the third layer buffer. The sequence is called copy in progress (CIP).
  (e.g. Page size=128 , CIP =128* 16 = 2048 clock cycle =2048 *16ns = 32us) (worth case scenario)
  SRAM256x16/ ChGRP16a
Notes: (CIP/ writing is trigger free/readout related to trigger)

## Slide 35: Second layer buffer
  SRAM256x16/ ChGRP16a

## Slide 36: Third layer buffer
Buffer size =1 K
  (Page size)*(Number of Pages) = 1024, user defined.
  Hit filling during CIP
  Readout from VME IRQ
  Outbuffer1k

## Slide 37: Fixed problem (Sep. 2012)
Some channels droped the hits, and some channel picked them up
This problem is fixed by adding one more clock cycle